## Slide 1
A Brain-controlled On-screen
Assistive Keyboard
Media Engineering and Technology Faculty
German University in Cairo
Author: Maqarios Wagdy Tawadros Saleh Mohareb
Supervisor: Assoc. Prof. Seif Eldawlatly
Bachelor Thesis - Expository

## Slide 2
Disabled People
Ex. Motor Neuron Disease
(MND)

## Slide 3
Objective
Designing an on-screen keyboard that allows
disabled people to interact with computer
without physical contact

## Slide 4
Introduction to BCI
What is a BCI?
Peripheral Nervous System
So, what is the relation?

## Slide 5
Introduction to BCI
10 – 20 system
Types of BCIs

## Slide 6
Introduction to BCI
P-300
Visual Stimuli
Oddball Paradigm

## Slide 7
Methodology & Results

## Slide 8
Flow of Operation
Recording
Pre-processing
P-300 Classification
Moving Average
Z-Score
Decimation
Common Average Reference (CAR)
Average of Repetitions

## Slide 9
Flow of Operation - Recording
Emotiv EPOC+
Digitization Rate of 128/256Hz
14 Channels

## Slide 10
Flow of Operation - Preprocessing
12 intensifications
100ms per intensification
75ms with no intensification
15 repetitions
Average of Repetitions

## Slide 11
Flow of Operation - Preprocessing
Common Average Reference (CAR)
Filtered signal for channel c at time t
Average of raw signals of all channels at time t
Raw signal for channel c at time t

## Slide 12
Flow of Operation - Preprocessing
Moving Average
Filtered signal for channel c at time t
Average of M signal after time t

## Slide 13
Flow of Operation - Preprocessing
Z-Score
Filtered Signal for channel c at time t
Signal for channel c at time t
Mean of signals for channel c
Standard deviation of signals for channel c

## Slide 14
Flow of Operation - Preprocessing
Dimensionality Reduction Technique
Decimation
Take 1 Leave n
Without Decimation. Features = 14 * 128 = 1792
With Decimation=6. Features = 14 * 128/6 = 588

## Slide 15
Flow of Operation – P300 Classification
x11
x12
...
x1f
Channel 1
x21
x22
...
x2f
Channel 2
Channel 2
…
xZ1
xZ2
...
xZf
Channel Z
x1
x2
...
xzf
Concatenation
x =
x1
x2
...
xzf
X =
--------------------------------------------------------------------------------------------
x1
x2
...
xzf
…
x1
x2
...
xzf
Character 1
Character 2
Character Y

## Slide 16
Flow of Operation – P300 Classification
Line Equation
Score Equation
Row Equation
Column Equation

## Slide 17
Linear Discriminant Analysis (LDA)
Flow of Operation – P300 Classification

## Slide 18
Results
Competition's Dataset
BCI 2000, 3rd Competition, 2nd dataset
2 Subject; A and B
Digitization rate 256hz
64 Channels

## Slide 19
Results
Competition's Dataset
Chart: Accuracy For Subjects A and B Before & After Applying Filters
| 8 Channels, 0 → 800ms | 8 Channels, 200 → 600ms | 64 Channels, 0 → 800ms | 64 Channels, 200 → 600ms
Non-Filtered | 77 | 78 | 83 | 84
Filtered | 84.5 | 71.5 | 86.5 | 80

## Slide 20
Results
Recorded Dataset
Chart: Accuracy For Subjects C and D Before & After Applying Filters
| 14 Channels, 0 → 800ms | 14 Channels, 200 → 600ms
Non-Filtered | 53.6 | 46.67
Filtered | 73.33 | 46.67

## Slide 21
Conclusion
Brain controlled system that allows spelling
Accuracy obtained on the benchmark data is ~80%
Offline Accuracy obtained on the recorded data is ~70%
Online Accuracy obtained on the recorded data is ~80%

## Slide 22
Thank You